## Slide 1: data link Control layer (DLC) – ARQ protocols
Shanghai Jiao Tong University

## Slide 2: ARQ: retransmission strategies
Physical channels are not perfect and transmission error may occur
Errors can be detected by error detection codes, such as CRC
Upon detecting errors, the receiver DLC may request retransmission of the frame
When designing a retransmission protocols, one must consider
  Only ‘correct’ packets are released to upper layers, and no duplicates
  Retransmission does not have a significant impact on the link utilization

## Slide 3: Frame transmission models and assumptions
Some assumptions
  All errors can be detected
  Frames (who are not lost) are received in order
  All frames can eventually arrive after some (finite number of) retransmissions
  Frames may experience an arbitrary delay
Three common schemes
  Stop-and-Wait
  Go back N
  Selective Repeat
1
2
3
4
5
Node A
Node B
Correction reception
Frame lost
Error occurs

## Slide 4: Stop-and-Wait ARQ
A send a frame to B
  If B receives it error-free, it sends back ACK
  Otherwise it sends NAK
  A start to send next frame when ACK is received
  A re-send previous packet if NAK is received
Node A
Node B
ACK
NAK
ACK

## Slide 5: Problems with the simplest Stop-and-Wait ARQ
What happens if a frame is lost?
  Sender will wait forever, so does the receiver
  Hotfix #1: Can be resolved by timeout mechanism
  Hotfix #2: Can be further resolved by frame sequence number
But what happens if ACK/NAK is lost, or come late?
  Sender will re-send
  But receiver will not be able to tell whether this is a new one, or a re-sent one
Node A
Node B
ACK
New, or old?

## Slide 6: Problems with the simplest Stop-and-Wait ARQ
  Hotfix #3: the receiver ACKs not only the reception of a frame, but also the sequence number of the next expected frame
In the above example, receiver ACKs both received packet 1, but sender has no way to tell whether the second ACK is for packet 1, or packet 2
1
1
Node A
Node B
ACK
2
ACK
For 1, or 2?

## Slide 7: Finally the stop-and-wait strategy that works
The algorithm for A-to-B transmission
  Set the integer variable SN to 0
  Wait and accept a packet from the higher layer, assign number SN to the new packet
  Transmit the SNth packet in a frame with SN in the sequence number field
  If an error-free frame is received from B containing a request number RN greater than SN, increase SN to RN and go to step 2. If no such frame is received within some finite delay, go to step 3.
The algorithm for B-to-A transmission
  Set the integer variable RN to 0 and then repeat 2 and 3 forever.
  Whenever an error-free frame is received from A containing a sequence number SN equal to RN, release the received packet to the higher layer and increase RN.
  Transmit a frame to A containing RN in the request number field after some bounded delay, after receiving any error-free data frame from A.

## Slide 8: An example of Stop-and-wait
0
Node A
SN
RN
Node B
0
1
0
1
2
2
Packet 0 release to up layer
Packet 0 timed out
Update RN
Packet 1 received and released to up layer
Frame received with no error, send ACK (1)
ACK received, update SN
Frame received with no error, send ACK (1)
Packet 2 received and released to up layer
ACK received, update SN

## Slide 9: Correctness of stop and wait
Correctness means:
  A never-ending stream of packets can be accepted from higher layer at A and delivered to the higher layer at B in order and without repetitions or deletions
Assumptions
  All errors can be detected
  Initially no frame on link (SN = RN = 0)
  All frames can eventually arrive after some (finite number of) retransmissions, success with at least probability
  Frames may experience an arbitrary delay
Proof of Correctness in divided into two parts:
  Safety: every packet is delivered once and only once, and in order
  Liveness: can work forever to deliver packets

## Slide 10: Safety
Starting from packet 0
Receiver B releases packets in order, and up to, but not including RN-th
Upon receiving an error-free RN-th packet, B will increment RN and release it to up layer
The RN-th Packet is the only possible packet that can even been released next, hence in order

## Slide 11: Liveness
: A started to transmit packet
: B received packet and updated RN to
: A was ACKed and update SN to
To proof liveness, it is sufficient to show that and
i
i
Node A
Node B
SN
RN
i
i
i+1
i
i+1
i+1
t1
t2
t3
Notes: 表示过程不会停止
𝑡_1<𝑡_2<𝑡_3<∞表示过程不会停止

## Slide 12: Liveness argument
Let , be values of SN and RN at time
From the algorithms
  and are nondecreasing in
  Since is the largest request number received from B up to , for all
  Since packet is never transmitted before , ;
From 2 and 3,
is increased to at and is increased to at , then according to 2
Since , and A transmit repeatedly up to , hence is finite
B transmit repeatedly, and since , hence is finite
Notes: 发送n次成功的概率为，因此需要无穷次重发才能成功的概率为0，即说明在有限次内一定成功
发送n次成功的概率为(1−𝑃)^(𝑛−1) 𝑃，因此需要无穷次重发才能成功的概率为0，即说明在有限次内一定成功

## Slide 13: Stop and wait with binary SN and RN
Given the assumption that frames travel in order on the link, binary sequence number is sufficient
Note that either
  SN = RN (from ) or
  SN = RN – 1 (from )
0
0
Node A
Node B
SN
RN
0
0
1
0
1
1
t1
t2
t3
Since all packets are transmitted in order on the link, only a single bit is enough to distinguish between the above cases
  RN = 0 and SN = 0, or RN = SN = 1
  RN – SN = 1
Notes: 本质原因是SN和RN至多差1

## Slide 14: Efficiency of stop and wait
0
Node A
SN
RN
Node B
1
: the time between transmission of a packet and receiving its ACK
: transmission time of the frame
: transmission time of the ACK
: propagation delay on the link
Efficiency of stop and wait if there is no errors

## Slide 15: Efficiency of stop and wait in presence of errors
: probability that a transmission error may occur either for packet frame or ACK
Besides the time needed in the normal (no error) case, i.e. , additional time is caused by timeouts
How many timeouts will happen?
So the extra time to wait is , where is the timeout interval
Thus the efficiency in presence of errors is:
Notes: 成功的概率是1-P，由几何分布可知成功前平均经历的次数为1/(1-P)-1=P/(1-P)

## Slide 16: Go back n ARQ
Also called sliding window ARQ
Receiving DLC at B operates in the same way
Sending DLC at A sends packets according to a sequence number window
  The window has fixed size n, and it starts with the most recently received requested number
Node A
0
2
Node B
SN
RN
1
3
4
5
6
0
1
0
2
3
4
5
Window
0
1
2
3
4
5
Packet released
[0,6]
[1,7]
[2,8]
[3,9]
[4,10]
Piggyback is used at B

## Slide 17: Example: Go back 4 in the case of transmission error in data packets
Error occurred during packet 1 transmission
Packets 2-4 will not be accepted until packet 1 is correctly released
When window is run out, A goes back 4 and start from 1 again
Node A
0
2
Node B
SN
RN
1
3
4
1
0
1
1
1
1
1
1
Window
0
1
Packet released
[0,3]
[1,4]
[2,5]
2
3
2
2
3
4
3

## Slide 18: Example: Go back 4 in the case of transmission error in ACK packets
Error occurred during ACK with RN = 1 transmission
Since ACK with RN=2 is received in time, window in A is advanced, no going back operation is needed
ACK with RN=3 is received with error, causing a going back operation
Node A
0
2
Node B
SN
RN
1
3
4
0
1
2
3
4
5
Window
0
Packet released
[0,3]
[2,5]
1
2
3
5
2
4
4
[4,7]
5
6
[5,8]
5
Notes: 对返回丢包的容忍度大一些

## Slide 19: Example: Effect of delayed feedback for go back 4
Delayed feedback (piggybacking and long frames in reverse direction) may cause a going back operation
Node A
0
2
Node B
SN
RN
1
3
4
0
1
3
4
5
Window
0
Packet released
[0,3]
[1,4]
1
2
3
1
3
4
4
[3,6]
[4,7]
5

## Slide 20: Go back N transmission algorithm at A
Let
  : the smallest number yet to be ACKed
  : the next packet to be accepted from the higher layer
Set and to 0
Do steps 3, 4 and 5 repeatedly in any order
If , and if packets are available from the higher layer, accept one packet into the DLC, assign to it and increment
If an error-free frame is received from B containing a request number RN greater than , increase to
If , and no frame is currently in transmission, choose some number , , transmit the packet with as sequence number.
Notes: 条件5：1) DLC虽然不从上层接受新包或者上层没有新包需要DLC发送；2) 序号为SNmin到SNmax-1之间的包已经发送但未收到确认。此时可以重新发送这些未确认的包。

## Slide 21: Example: Evolution of SNmax and SNmin
Node A
0
2
Node B
SN
RN
1
3
4
0
1
3
4
5
Window
0
Packet released
SNmin=0
[1,4]
1
2
3
1
3
4
4
[3,6]
[4,7]
5
SNmax=1
SNmin=0
SNmax=2
SNmin=0
SNmax=3
SNmin=1
SNmax=4
Notes: 在发完第4个包之后，条件3已经不满足，系统停止接受新包。此时条件5被触发，于是开始从序号为SNmin=1的包开始发送。

## Slide 22: Go back N transmission algorithm at B
Set RN to 0 and repeat steps 2 and 3 forever
Whenever an error-free frame is received from A contains a sequence number SN equal to RN, release the frame to the higher layer and increment RN
At arbitrary times, but within bounded delay after receiving any error-free data frame from A, transmit a frame to A containing RN in the request number field

## Slide 23: Efficiency of an ideal Go Back N
We want to choose large enough to allow continuous transmission while waiting for an ACK for the first packet of the window
  
Without errors the efficiency of an ideal Go Back N is
Pkt
Node A
SN
RN
Node B
ACK
DTP
DP
DTA
DP
S
Pkt
Pkt
Pkt
Pkt
nDTP

## Slide 24: Efficiency when there are errors
: probability that a frame arriving at B contains errors
: expected number of transmitted frames from A to B per successfully accepted packet at B
Assumption:
  A is always busy transmitting frames
  Error of successive frames is independent
can be derived recursively
It follows that the efficiency (or throughput)
Notes: 递归的要点是，每次重发的时候都跟以前发包的情况无关

## Slide 25: Notes on go back N
No buffering required at the receiver
Sender must buffer up to N packets while waiting for their ACK
Sender must re-send entire window in the event of an error
Packets can be numbered modulo where
  Because at most N packets can be sent simultaneously
Receiver can only accept packets in order
  Receiver must deliver packets in order to higher layer
  Cannot accept packet before packet
  This removes the need for buffering
  This introduces the need to re-send the entire window upon error
The major problem with Go Back N is this need to re-send the entire window when an error occurs. This is due to the fact that the receiver can only accept packets in order

## Slide 26: Selective Repeat Protocol (SRP)
Selective Repeat attempts to retransmit only those packets that are actually lost (due to errors)
  Receiver must be able to accept packets out of order
  Since receiver must release packets to higher layer in order, the receiver must be able to buffer some packets
Retransmission requests
  Implicit: The receiver acknowledges every good packet, packets that are not ACKed before a time-out are assumed lost or in error.
  Explicit: An explicit NAK (selective reject) can request retransmission of just one packet. This approach can expedite the retransmission but is not strictly needed
  One or both approaches are used in practice

## Slide 27: SRP Rules
Window protocol just like GO Back N, with window size
Packets are numbered modulus where
Sender can transmit new packets as long as their number is within of all un-ACKed packets
Sender retransmits un-ACKed packets after a timeout
Receiver ACKs all correct packets
Receiver stores correct packets until they can be delivered in order to the higher layer

## Slide 28: Buffering in SRP
Sender must buffer all packets until they are ACKed
  Up to un-ACKed packet are possible
Receiver must buffer packets until they can be delivered in order
  i.e., until all lower numbered packets have been received
  Needed for orderly delivery of packets to the higher layer
  Up to packets may have to be buffered (in the event that the first packet of a window is lost)
Implication of buffer size =
  Number of un-ACKed packets at sender
    Buffer limit at sender
  Number of un-ACKed packets at sender cannot differ by more than
    Buffer limit at the receiver (need to deliver packets in order)
  Packets must be numbered modulo (using bits)

## Slide 29: Efficiency of SRP
Ideally, in SRP, only packets containing errors will be retransmitted
  But sometimes packets may have to be retransmitted because their window expired. However, if the window size is set to be much larger than the timeout value then this is unlikely
With ideal SRP, efficiency (SRP)
  : probability of a packet error
Notice the difference with Go Back N where
  efficiency (Go Back N)
When the window size is small performance is about the same, however with a large window SRP is much better
  As transmission rates increase we need larger windows and hence the increased use of SRP

## Slide 30: Framing
Three types of framing used in practice
  Character-based framing
    Use special characters for idle fill and frame delimiter
  Bit-oriented framing with flags
    Use a string of bits called flags for idle fill and delimiter
  Length counts framing
    Use a length field in the header
001010100010010101010100000101011110100011110000111111100011100
How to determine the start and ending of a frame?

## Slide 31: Character Based Framing
Standard character codes such as ASCII and EBCDIC contain special communication characters that cannot appear in data
Entire transmission is based on a character code

## Slide 32: Issues with character based framing
Character code dependent
  How to send binary data instead of text?
  Can use transparent mode (DLE – Data Link Escape)
Frames must be integer number of characters
Errors in control characters can cause serious problems, such as frame loss (e.g. error in ETX)
Is a primary framing method from 1960 to ~1975, ARPANET

## Slide 33: Bit Oriented Framing (Flags)
A flag is some fixed string of bits to indicate the start and end of a frame
  A single flag can be used to indicate both the start and the end of a packet
In principle, any string could be used, but appearance of flag must be prevented somehow in data
  Standard protocols use the 8-bit string 01111110 as a flag
  Use 01111111..1110 (<16 bits) as abort under error conditions
  Constant flags or 1's is considered an idle state
Thus 0111111 is the actual bit string that must not appear in data in transmission
INVENTED ~ 1970 by IBM for SDLC (synchronous data link protocol)

## Slide 34: Bit stuffing at sender
Used to remove flag from original data
A 0 is stuffed after each consecutive five 1's in the original frame
1111110111111111110111110
Original data
0
0
0
0
Stuffed bits
Why is it necessary to stuff a 0 in 0111110?
because otherwise, the receiver will not be able to tell whether the final 0 is a stuffed 0, or original one
Notes: 在接收端看来，如果发射端在每5个1之后都插入0，那么0111110最后一个0一定是填充的0。如果发射端在0111110的第5个1之后不插入0的话，那就会引起歧义，到底是发送端故意插入的0呢，还是原来就有的0。

## Slide 35: De-stuffing at receiver
If 0 is preceded by 011111 in bit stream, remove it
If 0 is preceded by 0111111, it is the final bit of the flag
1001111101100111011111011001111110
remove
remove
End of frame

## Slide 36: Homework
2.36
2.37